## Slide 1: Sawtooth Weir Fish Passage
David Venditti
Sylvia Hamilton
Kurt Tardy
May 8, 2024

## Slide 2: Trap Status
Compliance Issues
Chinook
  Works well early and in higher water years
  Efficiency drops in July / August
Sockeye
  Return while efficiency low for Chinook
  Does collect some sockeye
    Only one (1) natural fish entered in 2023

## Slide 3: Chinook Effects
Trap Operation
  Low flow passage issues
  Circular ladder design
  May limit broodstock collection
Dropout below weir
  Integrated evaluation
  PNI effects

## Slide 4: Sockeye Effects
Trap Operation
  Same as Chinook
  Reduces time in natal lakes
    Effects?
  May spawn in the Salmon River
Particularly for Pettit adults
  May drop back to Redfish Lake
  Need to truck
    Not a permanent solution
    Eliminates volitional return to Pettit Lake

## Slide 5: Causes?
Water level and flow effects*
Temperature effect
Trap entrance
  Apron • THE HOLE
  Eddy below
Turn pools in ladder
Velocity in Ladder
  Removed PIT arrays
  In and out behavior

## Slide 6: Fish in the Hole
Regardless of the cause
  This is what happens

## Slide 7: Improvise and Overcome
Round-ups
  Chinook
  Sockeye
Band-aide
  ≈ 40 people
  ≈ $10 K
    Not a permanent fix
    Safety

## Slide 8
= Temperature differential
Observed temperature differential
Ideal velocity and direction
Alterations achieved through use of dam boards and plastic tarps
Ladder Entry Adjustments

## Slide 9: 2022-Improve Trap Entry
Previous “V” entry
New pivot bar entry
Fish seen leaving trap from “V” entry
Pivoting bars allow entry but no exit
Used for BY22 Chinook
Didn’t work great for other species

## Slide 10: 2022-New Ladder Configuration
First step of the First Dam boards blocking the rest of the ladder
der showing how ladder is blocked off
First step of the ladder straight into last step of ladder, then trap entrance
of the ladder straight into last step of ladder, then trap entrance

## Slide 11: 2023-Ladder Improvement
Added fencing to narrow the final step of the ladder so fish have a more direct path into the trap entrance
Added an opening to lower the velocity of the waterfall to lower the jump height

## Slide 12: 2023-Trap Improvement
Fish swim through the old trap entrance directly into the holding pond (yellow arrows)
Initially operated until first sort in mid August, then returned to using old trap
2023 converted West pond to the trap after the first sort (red arrow)
Use the crowder to separate freshly trapped fish from surplus fish
  Surplus fish are operculum punched and placed behind the crowder
  Designing a crowd rack to fit in the new trap space

## Slide 13: 2023-Trap Improvement
A finger weir was installed at the end of the holding pond to help retain fish
Fish no longer observed lingering in ladder
  Successful trapping of multiple species, including Rainbow, Cutthroat, and Bull Trout, as well as Sockeye

## Slide 14: Hyper-Infuser
Tested in 2022
  Too late for Chinook
Strips N2 from water
Replaces with O2
  Run through ladder
Creates attraction
  Not for sockeye

## Slide 15: Future Fixes

## Slide 16: Open Another Path

## Slide 17: Fish Corral
Pull panel on a bay
Picket in a trap box
Damaged panel in 2022
  Sockeye passed
  Proof of concept
Pull panels earlier
Fish Zone

## Slide 18: Fill the Hole
Create a riffle
  Eliminate holding area
  Force fish to ladder
  Designs drawn
Work window
  Jul. 15 – Aug. 15
  3 wk / ≤ 7 d in-water
  Trap closure

## Slide 19: Rebuild Weir & Ladder
LSRCP $200M Capital Maintenance
  SAW weir top of list
  2026’ish
Creative Funding
  Begin design work sooner?

## Slide 20: River Processes
2016
2023
34 m
34 m
19.5 m